## Slide 1: Frequency Stabilization of a Diode Laser to the RB D2 Transition
Charlotte Zehnder*, Will Bodron**, Wolfgang Korsch**
*Middlebury College, **University of Kentucky

## Slide 2
Why is a Stable Laser Necessary?
Small amounts of Rb and K will be present in the target due to spin exchange optical pumping.
A laser emitting a frequency on resonance with a transition of Rb maximizes the rotation of linearly polarized light due to the Faraday effect.
Small magnetic fields due to the spin-polarized 3He nuclei can be measured because of this effect, given the laser's frequency remains stable over a long enough time frame.
Target Cell
Rb
K
Pumping Chamber
Polarized 3He
3He
Rb
K

## Slide 3
Why is Frequency Stabilization Needed?
Lens
Laser Diode
Mirror
Temperature changes, air currents, and vibrations can cause laser drift.
We can change the position of the grating and current of the laser to keep the frequency stable
Blazed
Grating

## Slide 4
Rb D2 Transition
384230. 406 GHz
F’=4

## Slide 5
Spectroscopy Method
Horizontally Polarized Light
M1
M3
M2
PD1
PD2
PD1: Doppler-Free Signal
PD2: Doppler Broadened Signal
Evacuated cell contains diffuse Rb gas
Tested powers down to 2mV
Scan range from 384226 GHz to 384238 GHZ

## Slide 6
Doppler-Free Absorption Spectroscopy
87Rb
F=2
85Rb
F=3
85Rb
F=2
87Rb
F=1

## Slide 7
Doppler-Free Spectrum
85Rb
F=2
87Rb
F=2
85Rb
F=3
87Rb
F=1

## Slide 8
PID Laser Lock
Response
Lock-In Method:
Use frequency modulation and demodulation to produce an error signal PID input
Proportional Integral Derivative functions control laser current and piezo voltage
85Rb
Transition Peaks
F’=4
*See talk by Will Bodron

## Slide 9
Results

## Slide 10
Summary
Locked a near infrared laser to the doppler-free D2 transition of Rb using saturated absorption spectroscopy.
Used Top-of-Fringe methods to derive an error signal for PIDs controlling the laser current and piezo voltage on the Littrow grating.
Reduced laser drift by a factor of 100.

## Slide 11
Acknowledgements
This material is based upon work supported by the U.S. National Science Foundation under Award Number PHY-1950795 (UK REU) and the U.S. Department of Energy, Office of Science, Office of Nuclear Physics, under Award Number DE-FG02-99ER41101."

## Slide 12
References

## Slide 13
Crossover Frequencies
384230. 406 GHz
CO 34